Lincoln Pond CSLAP 4 year report

Secchi Disk

3.1 to 5.75 meters ave = 4.2

Total P

.003 to .014 mg/l ave = .008

NO3

.01 to .01 mg/l ave = .01 which means undetectable by DEC methods

T Color

6 to 25 platinum color units ave = 13

pH

6.34 to 7.98 ave = 7.26

Specific Conductivity

110 to 146 ave = 128 umho/cm at 25(C

Chlorophyll a

0.42 to 4.88 ave = 2.58 ug/l

Survey Question - physical condition

Not quite crystal clear to definite algae greenness

Survey Question – plants populations

Visible under water to dense growth at lake surface (this was in 1997 before our project)

Survey Question – recreational suitability

Very minor to substantially impaired in areas.